Tetris Protocol Description
This document covers the observed implementation of hex value transfers over the link cable on the original Gameboy version of Tetris.

This document is provided according to the terms of the GNU General Public License v3.0

Written by Eris C. and Isabella C.

Table of Contents

1.1 Clarification of Terms
In this document various terms refer to each connected system. The Originator system is the first one to select the 2 Player option, in this document, it is shortened to “Orig.”. In standard SPI this is also referred to as the Controller, formerly known as the “master” device.

The Receiver system is the 2nd player in the game and is shortened to “Recv.”. In standard SPI this is referred to as the peripheral device, formerly known as the “slave” device.

1.2 Methodology
In our testing and debugging we have used 2 methods to derive the data in this documentation.
We have used the BGB emulator to view the data sent over the link cable and tested these observations against a real game using a self-developed link cable emulator.

1.3 Misc Data
Integer	Hex	Usage	Notes
41	29	Start 2 player mode	Orig
0-17	00-11	Height Data	Applies to both Orig. and Recv.
96	60	Move From Level	Orig.
80	50	Move From Music	Orig.

1.4 Music Data
Integer	Hex	Usage	Notes
28	1C	A type music	Orig. Only
29	1D	B type music
30	1E	C type music
31	1F	Music off

1.5 Level Data
Integer	Hex	Usage	Notes
0	00	Level 0	Applies to both Orig. and Recv.
1	01	Level 1
2	02	Level 2
3	03	Level 3
4	04	Level 4
5	05	Level 5

1.6 Tetromino Data
Integer	Hex	Usage	Notes
0	00	L Tile	Names based on wiki
4	04	J Tile	Orig. Only
8	08	I Tile
12	0C	O Tile (Square)
16	10	Z Tile
20	14	S Tile
24	18	T Tile

Annotated Sample Data
Comments ending with (SO) are data only sent once, ones ending with (RS) are sent until the screen changes. Color-coded comments are matched to their color-coded blocks

A 55 29	Start Game (SO)

A 39 1C	Music A (RS)
A 39 1D	Music B (RS)

A 39 50	Move to level screen (SO)

A 00 00	Level 0, Level 0 (RS)
A 00 01	Level 0, Level 1 (RS)

A 00 60	Move to game (SO)
A 55 29	Start Game (SO)

These red bits are the shared junk data both games get at the start, decoding will be done in a later commit. Below is an uncondensed sample.

A 00 84
A 00 80
A 00 86
A 00 86
A 00 87
A 00 2F
A 00 2F
A 00 84
A 00 85
A 00 2F
A 00 2F
A 00 2F
A 00 85
A 00 2F
A 00 86
A 00 80
A 00 83
A 00 2F
A 00 81
A 00 2F
A 00 83
A 00 2F
A 00 87
A 00 2F
A 00 2F
A 00 83
A 00 2F
A 00 2F
A 00 87
A 00 2F
A 00 84
A 00 80
A 00 81
A 00 82
A 00 85
A 00 2F
A 00 84
A 00 80
A 00 86
A 00 84
A 00 84
A 00 84
A 00 87
A 00 2F
A 00 80
A 00 81
A 00 2F
A 00 82
A 00 84
A 00 83
A 00 81
A 00 2F
A 00 2F
A 00 85
A 00 2F
A 00 2F
A 00 2F
A 00 2F
A 00 2F
A 00 83
A 00 2F
A 00 85
A 00 2F
A 00 2F
A 00 2F
A 00 85
A 00 2F
A 00 2F
A 00 2F
A 00 2F
A 00 85
A 00 2F
A 00 86
A 00 85
A 00 2F
A 00 85
A 00 2F
A 00 2F
A 00 80
A 00 84
A 00 2F
A 00 2F
A 00 87
A 00 2F
A 00 81
A 00 2F
A 00 2F
A 00 81
A 00 2F
A 00 2F
A 00 2F
A 00 84
A 00 2F
A 00 2F
A 00 2F
A 00 83
A 00 2F
A 00 82
A 00 82
A 00 85

A 55 29	Start Game (SO)

A 00 08	8 tetromino sample, game sends 256 tetrominos
A 00 0C
A 00 14
A 00 00
A 00 08
A 00 14
A 00 08
A 00 00

A 56 30
A 30 00
A 00 02
A 44 02
A 44 20
A 44 02
A 44 02
A 00 02

A 00 03
A 00 03

A 00 94	Pause (RS)

A 00 03	Same data continues but player 2 acknowledges unpause after 2 bytes
A 00 03
A FF 03
A 00 03

A 11 06	Level 17, Level 6 (RS)

A AA 06
A FF 06
A FF 02
A 34 02

A 34 43	Game is over, data transmission stops until a new game is started